## Slide 1
RV College of
Engineering
Go, change the world
IOT & Embedded Computing
Programming LPC 2148 UART[Serial Port] Programming
Course Code:CS344AI

## Slide 2: Go, change the world
RV College of
Engineering

## Slide 3: Go, change the world
RV College of
Engineering
LPC 2148 UART0 & UART1 Unit...

## Slide 4: Go, change the world
RV College of
Engineering
LPC 2148 UART0 & UART1 Unit...

## Slide 5: Go, change the world
RV College of
Engineering
Asynchronous Serial Data Format...

## Slide 6: Go, change the world
RV College of
Engineering
RS 232 Interface

## Slide 7: Go, change the world
RV College of
Engineering
UART Registers..

## Slide 8: Go, change the world
RV College of
Engineering
Example: U0LCR = (0x03<<0) | (1<<7); 8bit data, 1Stop bit, No parity

## Slide 9: Go, change the world
RV College of
Engineering

## Slide 10: Go, change the world
RV College of
Engineering
BaudRate Calculation..

## Slide 11: Go, change the world
RV College of
Engineering
Configure UART for 115200 baud rate, PCLK = 15MHz
void uart_init(void)
{
//configurations to use serial port, UART0
PINSEL0 |= 0x00000005; // P0.0 & P0.1 ARE CONFIGURED AS TXD0 & RXD0
//programming the baud rate
U0LCR = 0x83; /* 8 bits, no Parity, 1 Stop bit & DLAB = 1 */
U0DLM = 0; U0DLL = 8; // 115200 baud rate, PCLK = 15MHz
U0LCR = 0x03; /* 8 bits, no Parity, 1 Stop bit & DLAB = 0 */
}
Calculation:
DLM:DLL = 15000000 / 16 * (115200) = result
Hence, DLL = result % 256 = 8 (lower 8 bits of result)
DLM = result / 256 (upper 8 bits of result)
(or , use calculator, convert answer in decimal to HEX, take lower two digits put into DLL, next two digits to DLM)

## Slide 12: Go, change the world
RV College of
Engineering
Write a Program to transmit a string from LPC 2148 to PC using Serial port / UART0
int main()
{
unsigned char i=0,ch,msg[]={"RVCE-CSE"};
SystemInit(); // set PCLK = 15MHz
uart_init(); // refer previous explanation
while((ch=msg[i++])!= '\0')
{
// Wait for Previous transmission to complete
while((U0LSR & (1u<<5))== 0x00){};
// Load the data to be transmitted
U0THR= ch;
}
}

## Slide 13: Go, change the world
RV College of
Engineering
Write a Program to transmit a string from LPC 2148 to PC using Serial port / UART0

## Slide 14: Go, change the world
RV College of
Engineering
Write a Program to receive a character from PC and output the 8 bit data on P0.16 to P0.23.
int main()
{
unsigned char i=0;
SystemInit();
uart_init();
IO0DIR = 0XFF << 16; // configure P0.16 to P0.23 as output pins
do
{
while((U0LSR & (0x01<<0))== 0x00){}; // wait till, a character (8bit) is received from PC
i = UORBR; // read from the UART0
IO0CLR = 0XFF << 16;IO0SET = U0RBR << i; // output the i(8bit code) to P0.16 – P0.23
}
while(1);
}

## Slide 15: Go, change the world
RV College of
Engineering
Write a Program to receive a character from PC and output the 8 bit data on P0.16 to P0.23.